## Slide 1: DCC2GO Basic Knowledge on DCCs
Information for technical staff at NMIS and DIs
Author list

## Slide 2: Today’s production life cycle
Calibration
1
start of
calibration
2
measure-
ment
3
data analysis
4
report
6
QM
7
production
8
Optimi-
sation
5
T
ransfer
9
time for re-
calibration
Industry
© figure: S. Hackel, et al, PTB, 2019
Life cycle of “calibration – use – recalibration” of measuring equipment

## Slide 3: Today’s production life cycle
Calibration
1
start of
calibration
2
measure-
ment
3
data analysis
4
report
6
QM
7
production
8
Optimi-
sation
5
T
ransfer
9
time for re-
calibration
Industry
© figure: S. Hackel, et al, PTB, 2019
NMI & DI (calibration laboratory) start of working with DCCs
Manually creating first calibration reports in machine-readable DCC format
Importing (reading) data from DCC of (in-house) calibrated equipment to QM system

## Slide 4: DCC examples
DCC by XML document
DCC by PDF document
<XML/>
DCC
PDF/A-3
DCC
PDF document providing human readable information and containing
Additional machine readable files with calibration result data
Fully XML structured file with all calibration information and data in machine-readable format
Optional human readable file (such as PDF) included as binary machine-readable data

## Slide 5: Example: PDF A/3 Type DCC
Example from Task 2.1?

## Slide 6: Example: XML Type DCC (1/3)
Fundamental DCC-layout
1. Administrative shell (mainly mandatory)
2. Calibration results (partly regulated)
3. Individual information (not regulated)
4. Optional Attachment:
„Human readable document“ (e. g. PDF)
+ Framework conditions
+ legal requirements
CODATA
17025
GUM
VIM
SI
…

## Slide 7: Example: XML Type DCC (2/3)
<XML/>
DCC
Human-readable
to
machine-readable
PTB-Certificate-1.81-17.019.pdf
PTB-DCC-1.81-17.019.xml
https://doi.org/10.5281/zenodo.3816696

## Slide 8: Example: XML Type DCC (3/3)
<XML/>
DCC
Human-readable
to
machine-readable
https://doi.org/10.5281/zenodo.3816696

## Slide 9: IT Requirements
Official documentation and resources:
https://dccwiki.ptb.de/en/DCC_basic_ideas
https://www.ptb.de/dcc/
Start working with XML type DCCs
An office computer is sufficient to start reading and writing XML DCCs
People experienced with XML may use standard text & code editors such as Notepad, Notepad++, Visual Studio
PTB offers the GEMIMEG TOOL which is a prototype web service for creating and reading DCCs with a user interface for people without experience in XML. The XML is created by the web service
https://www.gemimeg.ptb.de/gemimeg-tool/#/

## Slide 10: Today’s production life cycle
Calibration
1
start of
calibration
2
measure-
ment
3
data analysis
4
report
6
QM
7
production
8
Optimi-
sation
5
T
ransfer
9
time for re-
calibration
Industry
© figure: S. Hackel, et al, PTB, 2019
NMI & DI (calibration laboratory) start of working with DCCs
First DCCs transferred to customers as appendix to existing analogue certificates

## Slide 11: Today’s production life cycle
Calibration
1
start of
calibration
2
measure-
ment
3
data analysis
4
report
6
QM
7
production
8
Optimi-
sation
5
T
ransfer
9
time for re-
calibration
Industry
© figure: S. Hackel, et al, PTB, 2019
NMI & DI (calibration laboratory) advancing DCC transfer
DCC with electronic or digital signature of person or seal of calibration lab (for trust)
Calibration lab providing software (web) interface for DCC transmission / retrieval
Change of default format from analogue to DCC

## Slide 12: Role of digital signatures and seals
Correct DCC from the Calibration Laboratory
Providing DCC Integrity
(no modifications)
Providing DCC Authenticity
(from our "lab")
DCC Exchange
Calibration
Laboratory
Calibration
Customer
E.g. Digital Signature
Confidential transmission
(encryption)

## Slide 13: IT Requirements
Start working with electronic and digital signatures
An office computer is sufficient to start working with electronic and digital signatures
Most PDF viewing and editing software allows to create simple electronic signatures that allow a low level protection of PDF documents against manipulation.
Qualified digital signatures for documents (XML, PDF, …) and document containers (folders) are more advanced and start working with this will need additional equipment:
Signer’s
Key Card
  Software to apply signature to files
  Private (secret) digital key code for signing on a key card
  Hardware device connected to computer via USB for reading the key card and authorising signature
The European Commission has a list of providers of trusted and recognized signatures
https://digital-strategy.ec.europa.eu/en/policies/eu-trusted-lists

## Slide 14: Today’s production life cycle
Calibration
1
start of
calibration
2
measure-
ment
3
data analysis
4
report
6
QM
7
production
8
Optimi-
sation
5
T
ransfer
9
time for re-
calibration
Industry
© figure: S. Hackel, et al, PTB, 2019
NMI & DI (calibration laboratory) advancing automation of DCC creation
Using software to automatically assemble administrative DCC data
Automated measurement processes and data collection in machine-readable formats
Automated evaluation of data for calibration report and assembly of DCC measurement results

## Slide 15: Today’s production life cycle
Calibration
1
start of
calibration
2
measure-
ment
3
data analysis
4
report
6
QM
7
production
8
Optimi-
sation
5
T
ransfer
9
time for re-
calibration
Industry
© figure: S. Hackel, et al, PTB, 2019
NMI & DI (calibration laboratory) advancing automation of DCC usage
QM software automatically retrieving DCCs and importing data in company data bases
Various processes where measure-ment data of equipment is automatically enhanced with metadata from DCC, e.g., measurement uncertainties, etc.

## Slide 16: IT Requirements
Some areas of a organization may already have laboratories where software and IT infrastructure has been established that allows an automatic processing of a calibration and the automatic creation of the Calibration Certificate (Word, PDF, or similar). Automatically creating a DCC would require only an additional output module for the software.
General requirements comprise for example
  Databases for storing measurement data, calibration data, administrative data for customers, equipment data, etc.
  Data exchange network allowing data exchange between digital outputs of measuring devices and software running the calibration (including instruments able to send and receive data)
  Software automating the calibration process (controlling devices etc., collecting and evaluating data as well as creating output reports)
In case of the XML type DCC, first commercial tools are available
such as AnyDCC (© 2022 Stotz Software)

## Slide 17: Today’s production life cycle
Calibration
1
start of
calibration
2
measure-
ment
3
data analysis
4
report
6
QM
7
production
8
Optimi-
sation
5
T
ransfer
9
time for re-
calibration
Industry
© figure: S. Hackel, et al, PTB, 2019
NMI & DI (calibration laboratory) advancing automation of services
Calibration laboratory offering portal where automatic processable requests for calibration services can be submitted

## Slide 18: IT Requirements
Calibration laboratory and customer will need access to the world wide web to be able to exchange relevant information
The calibration laboratory needs to operate an access point for customers, e.g., an application running on a web server (hosted or rent by laboratory) or an service establish through a cloud environment.
The service of the calibration laboratory could provide a Web Page for humans to manually enter and submit data and in addition have a programming interface through which software of a customer could automatically submit data.
The customer may need to register an account at the service provided by the laboratory to be enabled to digitally submit requests for calibration.
The customer may operate an equipment management system that automatically schedules and requests re-calibration.

## Slide 19: Machine-Interoperability
“Bad analogue data will create bad digital data”
Automation of processes and usage of data by machines will need machine-interoperable data ready for human-to-machine and machine-to-machine communication
Developments towards wider machine-interoperable DCCs include
Harmonization of formats like XML DCC
Harmonization of domain (measurand) specific calibration results & good practices
Harmonization of common identifiers (terms) for data and properties in DCCs
Where different DCC types are consumed, software for mapping between different data representations
Harmonization examples:
CIPM Digital-SI (format, SI identifiers) DKD committees (domain, good practice, identifiers)
XML DCC (format, identifiers) EURAMET TC-IM 1448 DCC (good practice, identifiers, mappings)

## Slide 20
Final page with contact information